## Slide 1: Linux Internals & Networking System programming using Kernel interfaces

## Slide 2: Inter Process Communications (IPC)

## Slide 3: Inter Process Communications Introduction
Inter process communication (IPC) is the mechanism whereby one process can communicate, that is exchange data with another processes
There are two flavors of IPC exist: System V and POSIX
Former is derivative of UNIX family, later is when standardization across various OS (Linux, BSD etc..) came into picture
Some are due to “UNIX war” reasons also
In the implementation levels there are some differences between the two, larger extent remains the same
Helps in portability as well

## Slide 4: Inter Process Communications Pipes
A pipe is a communication device that permits unidirectional communication
Data written to the “write end” of the pipe is read back from the “read end”
Pipes are serial devices; the data is always read from the pipe in the same order it was written
Water
In
End
Water
Out
End
Data
In
End
Data
in
Out

## Slide 5: Inter Process Communications Pipes – Direction of communication
Let's say a Parent wants to communicate with a Child
Generally the communication is possible both the way!
Parent
Child

## Slide 6: Inter Process Communications Pipes - Pros & Cons
PROS
Naturally synchronized
Simple to use and create
No extra system calls required to communicate (read/write)
Less memory size (4K)
Only related process can
communicate.
Only two process can communicate
One directional communication
Kernel is involved
CONS

## Slide 7: Inter Process Communications FIFO - Properties
A first-in, first-out (FIFO) file is a pipe that has a name in the file-system
FIFO file is a pipe that has a name in the file-system
FIFOs are also called Named Pipes
FIFOs is designed to let them get around one of the shortcomings of normal pipes

## Slide 8: Inter Process Communications FIFO – Working
User
Kernel
P1
P2
Pipe
Buffer
file

## Slide 9: Inter Process Communications FIFO - Creation
FIFO can also be created similar to directory/file creation with special parameters & permissions
After creating FIFO, read & write can be performed into it just like any other normal file
Finally, a device number is passed. This is ignored when creating a FIFO, so you can put anything you want in there
Subsequently FIFO can be closed like a file
Function | Meaning
int mknod( const char *path, mode_t mode, dev_t dev) | path: Where the FIFO needs to be created (Ex: “/tmp/Emertxe”) mode: Permission, similar to files (Ex: 0666) dev: can be zero for FIFO

## Slide 10: Inter Process Communications FIFO - Access
Access a FIFO just like an ordinary file
To communicate through a FIFO, one program must open it for writing, and another program must open it for reading
Either low-level I/O functions (open, write, read, close and so on) or C library I/O functions (fopen, fprintf, fscanf, fclose, and so on) may be used.
user@user:~] ls -l my_fifo
prw-rw-r-- 1 biju biju 0 Mar 8 17:36 my_fifo
prw-

## Slide 11: Inter Process Communications FIFO vs Pipes
Unlike pipes, FIFOs are not temporary objects, they are entities in the file-system
Any process can open or close the FIFO
The processes on either end of the pipe need not be related to each other
When all I/O is done by sharing processes, the named pipe remains in the file system for later use

## Slide 12: Inter Process Communications FIFO - Pros & Cons
PROS
Naturally synchronized
Simple to use and create
Unrelated process can
communicate.
No extra system calls required to communicate (read/write)
Work like normal file
Less memory size (4K)
Only two process can communicate
One directional communication
Kernel is involved
CONS

## Slide 13: Inter Process Communications Shared vs Local Memory
Process 1
Process 2
Process 3
Process n
Local
Memory
Local
Memory
Local
Memory
Local
Memory
Shared Memory
User
Space
Kernel
Space

## Slide 14: Inter Process Communications Shared Memories - Procedure
Create
Attach
Read/Write
Detach
Remove
95%

## Slide 15: Inter Process Communications Shared Memories – Function calls
Function | Meaning
int shmget( key_t key, size_t size, int shmflag) | Create a shared memory segment key: Seed input size: Size of the shared memory shmflag: Permission (similar to file) RETURN: Shared memory ID / Failure
void *shmat( int shmid, void *shmaddr, int shmflag) | Attach to a particular shared memory location shmid: Shared memory ID to get attached shmaddr: Exact address (if you know or leave it 0) shmflag: Leave it as 0 RETURN: Shared memory address / Failure
int shmdt(void *shmaddr) | Detach from a shared memory location shmaddr: Location from where it needs to get detached RETURN: SUCCESS / FAILURE (-1)
shmctl(shmid, IPC_RMID, NULL) | shmid: Shared memory ID Remove and NULL

## Slide 16: Inter Process Communications Synchronization - Debugging
The ipcs command provides information on inter-process communication facilities, including shared segments.
Use the -m flag to obtain information about shared memory.
For example, this image illustrates that one shared memory segment, numbered 392316, is in use:
user@user:~] ipcs -s
------ Semaphore Arrays --------
key semid owner perms nsems
user@user:~] ipcs -m | more
------ Shared Memory Segments --------
key shmid owner perms bytes nattch status
0x00000000 393216 user 600 524288 2 dest
0x00000000 557057 user 700 2116 2 dest
0x00000000 589826 user 700 5152 2 dest
Semaphores
In the
system
Shared
Memory
in the
system

## Slide 17: Signals

## Slide 18: Signals
Signals are used to notify a process of a particular event
Signals make the process aware that something has happened in the system
Target process should perform some pre-defined actions to handle signals
This is called ‘signal handling’
Actions may range from 'self termination' to 'clean-up'

## Slide 19: Signals Origins
The kernel
A Process may also send a Signal to another Process
A Process may also send a Signal to itself
User can generate signals from command prompt:
‘kill’ command:
$ kill <signal_number> <target_pid>
$ kill –KILL 4481
Sends kill signal to PID 4481
$ kill –USR1 4481
Sends user signal to PID 4481

## Slide 20: Signals Handling
When a process receives a signal, it processes
Immediate handling
For all possible signals, the system defines a default disposition or action to take when a signal occurs
There are four possible default dispositions:
  Exit: Forces process to exit
  Core: Forces process to exit and create a core file
  Stop: Stops the process
  Ignore: Ignores the signal
Handling can be done, called ‘signal handling’

## Slide 21: Signals Handling
The signal() function can be called by the user for capturing signals and handling them accordingly
First the program should register for interested signal(s)
Upon catching signals corresponding handling can be done
Function | Meaning
signal (int signal_number, void *(fptr) (int)) | signal_number : Interested signal fptr: Function to call when signal handles

## Slide 22: Signals Handling
User
Space
Signal handler
executed
Signals
S/w interrupt from
K/S to U/S
Kernel
Space
Pointer | Process State
Process ID | 
Signals | 
Registers | 
Memory Limits | 
List of Open Files | 
P1
Signal generated
Signal
handler
Registering handler
signal / sigaction

## Slide 23: Signals Handler
A signal handler should perform the minimum work necessary to respond to the signal
The control will return to the main program (or terminate the program)
In most cases, this consists simply of recording the fact that a signal occurred or some minimal handling
The main program then checks periodically whether a signal has occurred and reacts accordingly
Its called as asynchronous handling

## Slide 24: Signals Advanced Handling
The signal() function can be called by the user for capturing signals and handling them accordingly
It mainly handles user generated signals (ex: SIGUSR1), will not alter default behavior of other signals (ex: SIGINT)
In order to alter/change actions, sigaction() function to be used
Any signal except SIGKILL and SIGSTOP can be handled using this
Function | Meaning
sigaction( int signum, const struct sigaction *act, struct sigaction *oldact) | signum : Signal number that needs to be handled act: Action on signal oldact: Older action on signal

## Slide 25: Signals vs system calls
User
Space
Sending Signal
System call
S/w interrupt from
U/S to K/S
Signals
S/w interrupt from
K/S to U/S
P1
P2
Kernel
Space

## Slide 26: Signals Self Signaling
A process can send or detect signals to itself
This is another method of sending signals
There are three functions available for this purpose
This is another method, apart from ‘kill’
Function | Meaning
raise (int sig) | Raise a signal to currently executing process. Takes signal number as input
alarm (int sec) | Sends an alarm signal (SIGALRM) to currently executing process after specified number of seconds
pause() | Suspends the current process until expected signal is received. This is much better way to handle signals than sleep, which is a crude approach

## Slide 27: Process Management - Concepts

## Slide 28: Process Management - Concepts CPU Scheduling
Maximum CPU utilization obtained with multi programming
CPU–I/O Burst Cycle – Process execution consists of a cycle of CPU execution and I/O wait
:
load store
add store
read from file
wait for I/O
store increment
Index
write to file
wait for I/O
load store
add store
read from file
wait for I/O
:
CPU Burst
I/O Burst
CPU Burst
I/O Burst
CPU Burst
I/O Burst

## Slide 29: Process Management - Concepts States
terminated
exit
waiting
I/O or event wait
running
scheduler dispatch
new
admitted
ready
I/O or event completion
interrupted

## Slide 30: Process Management - Concepts States
A process goes through multiple states ever since it is created by the OS
State | Description
New | The process is being created
Running | Instructions are being executed
Waiting | The process is waiting for some event to occur
Ready | The process is waiting to be assigned to processor
Terminated | The process has finished execution

## Slide 31: Process Management - Concepts Schedulers
Selects from among the processes in memory that are ready to execute
Allocates the CPU to one of them
CPU scheduling decisions may take place when a process:
  Switches from running to waiting state
  Switches from running to ready state
  Switches from waiting to ready
  Terminates
Scheduling under 1 and 4 is non-preemptive
All other scheduling is preemptive

## Slide 32: Process Management - Concepts Scheduling - Types
Scheduling
Co-operative
Pre-emptive
First Come First
Serve (FCFS)
Priority Based
Round Robin:
Time-slice (TS) based
Round Robin:
Priority based
Static: Rate
Monotonic (RM)
Dynamic: Earliest
Deadline First (EDF)
Dynamic: Earliest Deadline First (EDF)

## Slide 33: Process Management - Concepts Scheduling – Types – Co-operative vs Pre-emptive
In Co-operative scheduling, process co-operate in terms of sharing processor timing. The process voluntarily gives the kernel a chance to perform a process switch
In Preemptive scheduling, process are preempted a higher priority process, thereby the existing process will need to relinquish CPU

## Slide 34: Process Management - Concepts Scheduling – Types – FCFS
First Come First Served (FCFS) is a Non-Preemptive scheduling algorithm. FIFO (First In First Out) strategy assigns priority to process in the order in which they request the processor. The process that requests the CPU first is allocated the CPU first. This is easily implemented with a FIFO queue for managing the tasks. As the process come in, they are put at the end of the queue. As the CPU finishes each task, it removes it from the start of the queue and heads on to the next task.

## Slide 35: Process Management - Concepts Scheduling – Types – FCFS
Process | Burst time
P1 | 20
P2 | 5
P3 | 3
Suppose processes arrive in the order: P1, P2, P3 , The Gantt Chart
for the schedule is
0
20
25
28
P1 | P2 | P3

## Slide 36: Process Management - Concepts Scheduling – Types – RR: Time Sliced
Processes are scheduled based on time-slice, but they are time-bound
This time slicing is similar to FCFS except that the scheduler forces process to give up the processor based on the timer interrupt
It does so by preempting the current process (i.e. the process actually running) at the end of each time slice
The process is moved to the end of the priority level

## Slide 37: Process Management - Concepts Scheduling – Types – RR: Time Sliced
Process | Burst time
P1 | 20
P2 | 5
P3 | 3
Suppose processes arrive in the order: P1, P2, P3 , The Gantt Chart
for the schedule is
P1 | P2 | P3
0
4
9
P1 | P1 | P1
12
17
22

## Slide 38: Process Management - Concepts Scheduling – Types – RR: Priority
Processes are scheduled based on RR, but priority attached to it
While processes are allocated based on RR (with specified time), when higher priority task comes in the queue, it gets pre-empted
The time slice remain the same

## Slide 39: Process Management - Concepts Scheduling – Types – RR: Time Sliced
Process | Burst time
P1 | 24
P2 | 10
P3 | 15
Suppose processes arrive in the order: P1, P2, P3 and assume P2
have high priority, The Gantt Chart for the schedule is
P1 | P2 | P3
0
4
11
P1 | P1 | P1
16
21
24

## Slide 40: Process Management - Concepts Scheduling – Types – Pre-emptive
Pre-emption means while a lower priority process is executing on the processor another process higher in priority than comes up in the ready queue, it preempts the lower priority process.
Rate Monotonic (RM) scheduling:
  The highest Priority is assigned to the Task with the Shortest Period
  All Tasks in the task set are periodic
  The relative deadline of the task is equal to the period of the Task
  Smaller the period, higher the priority

## Slide 41: Process Management - Concepts Scheduling – Types – Pre-emptive
Earliest Deadline First (EDF) scheduling:
  This kind of scheduler tries to give execution time to the task that is most quickly approaching its deadline
  This is typically done by the scheduler changing priorities of tasks on-the-fly as they approach their individual deadlines

## Slide 42: Process Management - Concepts Scheduling – Types – Rate Monotonic (RM)
T1 preempts T2 and T3.
T2 and T3 do not preempt each other.

## Slide 43: Process Management - Concepts Scheduling – Types – Earliest Deadline First (EDF)

## Slide 44: Thank You